## Slide 1
U2A SPID
  Support idea
2019.Nov.7
Megumi Yoshinaga
Renesas Electronics Corporation

## Slide 2: summary
Background
  U2A model doesn’t support SPID module function.
  Then the Master IPs which are provided SPID by SPID module can’t know own SPID and doesn’t set SPID at TlmG3mExtension (This means SPID is always 0).
  Bosch requested us to support SPID module (register and function).
  Then I considered how to support SPID module and connect with Master IP.
Purpose
  List up and compare the ideas and decide which idea is better.

## Slide 3: HW connection (from UM0.61 Figure 1.5)
SystemBus
P-Bus
H-Bus
ET NB1(M)
Gb Ether
ET NB0(M)
Fast Ether
FlexRay1
FlexRay0
RHSIF
SPID
registers
I-Bus
Inter-processor element bus
Inter-processor element bus
Bus transaction
SPID value

## Slide 4: Modeling idea (summary)
Idea1
  SPID module connect with each Master IP directly to input each SPID
  Master IP set SPID at the transaction (mSpId of TlmG3mExtension using setSpId())
Idea2
  SPID module connect with each SPID adder module which is connected between Master IP and bus
  Master IP is not needed to update to set SPID
  SPID adder module set SPID at the transaction which is sent by Master IP.
  SPID adder need to change the master I/F from Master IP to SPID adder module, before it sends transaction to bus.
  SPID adder need to change the master I/F from SPID adder module to Master IP, when it receives nb_transport_bw.

## Slide 5: modeling idea (pros cons)
Compare item | Idea1 | Idea2
Impact range (for master IP) | 1 point All Master IP which is provide SPID by SPID module need to update. | 5 point All Master IPs don’t need to update to support SPID.
Expandability (add the target master IP) e.g. E2x | 1 point When the target master IP which has been finished the development is added, that IP need to update. | 5 point All Master IPs don’t need to update to support SPID.
Additional IP | 5 point No additional IP | 3 point Need SPID adder module. But it is small module and there is reference module in common directly.
Ease for Integration | 5 point Connection spec is clear and simple. | 4 point Connection spec is clear and simple. But instance number is larger than Idea1.
Total | 12 point | 17point
I think idea2 is better idea
5 level score

## Slide 6: Model connection idea1
SystemBus
P-Bus
H-Bus
ET NB1(M)
Gb Ether
ET NB0(M)
Fast Ether
FlexRay1
FlexRay0
RHSIF
SPID
registers
I-Bus
Inter-processor element bus
Inter-processor element bus
Connected by signal
Bus transaction
SPID value

## Slide 7: Model connection idea2
SystemBus
P-Bus
H-Bus
ET NB1(M)
Gb Ether
ET NB0(M)
Fast Ether
FlexRay1
FlexRay0
RHSIF
SPID
registers
I-Bus
Inter-processor element bus
Inter-processor element bus
Connected by signal
SPID adder
Bus transaction
SPID value
SPID adder
SPID adder
SPID adder
SPID adder

## Slide 8: SPID Model idea 1
ET NB1(M)
Gb Ether
ET NB0(M)
Fast Ether
FlexRay1
FlexRay0
RHSIF
Connected by signal
SPID model
BusMaster 00 SPID mask register
BusMaster 00 SPID mask lockregister
BusMaster 31 SPID mask register
…
…
BusMaster 31 SPID mask lockregister
BusMaster 17 SPID register
BusMaster 19 SPID register
BusMaster 22 SPID register
BusMaster 23 SPID register
BusMaster 24 SPID register
BusMaster 25 SPID register
BusMaster 26 SPID register
ICUM_AES
ICUMHA
(ICUP)
H-Bus
ICUM P-Bus
ICUM SIC
Set SPID which is informed by SPID model into bus transaction
Set SPID which is informed by SPID model into bus transaction
ICUMHASS

## Slide 9: SPID Model idea 2
ET NB1(M)
Gb Ether
ET NB0(M)
Fast Ether
FlexRay1
FlexRay0
RHSIF
Connected by signal
SPID model
BusMaster 00 SPID mask register
BusMaster 00 SPID mask lockregister
BusMaster 31 SPID mask register
…
…
BusMaster 31 SPID mask lockregister
BusMaster 17 SPID register
BusMaster 19 SPID register
BusMaster 22 SPID register
BusMaster 23 SPID register
BusMaster 24 SPID register
BusMaster 25 SPID register
BusMaster 26 SPID register
ICUM_AES
ICUMHA
(ICUP)
H-Bus
ICUM P-Bus
ICUM SIC
Set SPID which is informed by SPID model into bus transaction
Set SPID which is informed by SPID model into bus transaction
ICUMHASS
SPID adder
SPID adder
SPID adder
SPID adder
SPID adder
SPID adder
SPID adder
SPID adder

## Slide 10: Request
H-Bus
Please consider the SPID model feature to support U2A and E2x
  Arai-san checked both HW UM. Here is his report.
    Registers
      BusMaster XX SPID Register ・・・XX：00~31 (Common spec b/w U2A and E2x)
      BusMaster XX SPID Mask Register ・・・XX：00~31 (Common spec b/w U2A and E2x)
      BusMaster XX SPID Mask Lock Register ・・・XX：00~31 (Common spec b/w U2A and E2x)
      SPID Key Code Protect Register ・・・(Common spec b/w U2A and E2x)
    The different point b/w U2A and E2x is the valid (used) register range (above XX)
    Then he think you can prepare SPID module for common IP.

## Slide 11
Renesas.com